## Slide 1
HIGHER ENGINEERING EDUCATION DEVELOPMENT (M-JEED) PROJECT
JOINT RESEARCH – BUSINESS INNOVATION PARTNERSHIP 2026
17 September 2026 | Section 4 · Energy & Renewable Energy, Room 4 | NUM Library Building, Ulaanbaatar
RESEARCH FIELD
Automation and Systems Engineering
Low-power toroidal-core energy harvester for a leaky feeder communication system in the UHF band
Keywords: energy harvesting · leaky feeder · toroidal ferrite core · UHF 411–422 MHz · wireless power transfer · underground IoT
IEICE Electronics Express (SCIE), 2026 · DOI: 10.1587/elex.23.20260374
1. PROBLEM & OBJECTIVE
Why underground IoT nodes need a battery-free power source
PROBLEM
• Underground IoT sensor nodes need reliable power, but replacing batteries frequently is difficult and costly in confined and hazardous tunnel environments.
• Conventional ambient sources — solar, thermal, vibration — are unavailable or unreliable deep underground.
• Leaky-feeder cables already run through every drift and radiate a continuous, controlled UHF field that has so far remained unused.
OBJECTIVE
• Develop a toroidal-core energy (TCE) harvester that extracts RF energy from the near field of a UHF leaky-feeder cable and converts it into usable DC power.
• Design and optimise the harvester in CST and validate it experimentally across the 411–422 MHz operating band.
• Deliver a clamp-on, non-intrusive module able to power low-power IoT sensor nodes without cutting or re-cabling the feeder.
2. APPROACH & COLLABORATION
Ferrite-core design, CST optimisation and the MUST – Sangmyung – KOICA partnership
APPROACH & TECHNOLOGY
• Harvester: NiZn K10 ferrite toroid (R63 × 38 × 25 mm) with a 7-turn copper winding, tuned to resonance at 416.5 MHz.
• Simulation: full-wave CST transient solver; the feeder is excited through a waveguide port and terminated in a matched 50 Ω load.
• Conversion chain: LC tank → HSMS-285P Schottky voltage doubler → RFD199A-PCB RF–DC converter → regulated DC output.
• Optimisation: three toroid sizes, permeabilities μi = 450 / 700 / 900 and turns N = 4…11 were swept to maximise flux capture below Bsat ≈ 0.45 T.
COLLABORATION
• MUST–SICT: design, CST modelling, fabrication and RF measurement (Radio Frequency and Antenna Lab.).
• Sangmyung University (Korea), Prof. Juhee Choi: rectifier chain and measurement methodology.
• KOICA: funding and lab capacity building (Contract No. P2019-00124).
3. KEY RESULTS, TECHNOLOGY / PRODUCT
Simulated and measured performance of the «TCE Harvester» and its product form
KEY RESULTS
• At the 416.5 MHz resonance the toroidal winding produced 6.83 V and 71.4 mA in simulation — an AC power-conversion efficiency of 48.8%.
• Simulation and measurement agree closely: measured |S₁₁| reaches −26.7 dB at 416 MHz against −18.7 dB in simulation.
• A 24 W UHF transmitter on a 5 m RLK78-50JFNA cable delivered 6.92 V DC and 166 mA across the fixed load.
• Regulated 4.7 V DC output — continuous operation of low-power IoT nodes above +30 dBm forward power, pulsed operation below that.
• A linear-scaling post-processing method overcomes the normalised port-power behaviour of CST, enabling rapid input-power parametric studies.
• The UHF leaky feeder is established as a viable in-tunnel energy source for IoT nodes.
4. APPLICATIONS & BUSINESS POTENTIAL
Where battery-free in-tunnel power matters, and how it reaches the market
APPLICATIONS
• Battery-free power for RSSI monitors, gas and dust sensors and tag readers along underground mine drifts.
• Tunnels, metro lines and infrastructure corridors where leaky feeders are already installed for radio coverage.
• Maintenance-free sensing in confined or hazardous spaces where battery changes require permits and downtime.
• Combined with the «RF Check Point» RTU project at MUST, for fully self-powered underground monitoring.
5. PARTNERSHIP, IMPACT & NEXT STEPS
What we are looking for, the expected impact and the roadmap to 2027
WE ARE LOOKING FOR:
☑ Pilot testing ☑ Joint R&D ☑ Technology transfer
☑ Licensing ☑ Commercialization / Investment
WHAT WE EXPECT FROM PARTNERS:
• Access to live leaky-feeder networks for field trials, support on active-rectifier design and certification, and co-authored publications.
6. CONTACT & BUSINESS MATCHING
B. Purevtseren (Ph.D) | MUST, SICT, Radio Frequency and Antenna Lab. e-mail: Purevtseren_b@must.edu.mn
Phone: +976-88772860
TECHNOLOGY / PRODUCT
• Product form: a clamp-on «TCE Harvester» module — ferrite toroid, winding, LC tank and rectifier board — fitted to an existing leaky feeder without cutting the cable.
• Core: NiZn K10 ferrite, R63 × 38 × 25 mm, N = 7 turns, 1 mm copper wire, 4.7 pF LC tank.
• Band: 411–422 MHz (resonance 416.5 MHz) — the band already used by mine leaky-feeder and TETRA-class radio systems.
• Output: 4.7 V regulated DC; 6.92 V and 166 mA measured at 24 W forward power.
• Advantages: no battery replacement, no additional cabling, non-intrusive installation, and it reuses infrastructure that already exists in every tunnel.
• Maturity: TRL 4–5 — validated on a laboratory leaky-feeder testbed and peer-reviewed in IEICE Electronics Express (SCIE), 2026.
BUSINESS POTENTIAL
• Clamp-on energy harvesting modules manufactured in Mongolia as an add-on to existing leaky-feeder infrastructure.
• Bundled with underground IoT sensor products to remove battery logistics from the customer's operating cost.
• Joint products, technology transfer and licensing with the Korean partner.
• Licensing of the ferrite-core and rectifier design to communications and mining-equipment suppliers.
• Engineering services: site survey, harvested-power measurement and installation on live feeder networks.
IMPACT
• Economic: removes battery replacement cost and downtime from sensor networks.
• Social: safer maintenance — fewer battery-change trips into confined and hazardous spaces.
• Environmental: fewer primary lithium batteries consumed and disposed of underground.
NEXT STEPS
Anudari Dashbaatar, Delgermurun Batbold,
Prof. Uuganbayar Purevdorj, Prof. Chuluunbandi Naimannaran
School of Information and Communication Technology, MUST
Prof. Juhee Choi (Ph.D)
Sangmyung University, Republic of Korea
Joint research code:
J23A16-1
MONGOLIAN PROJECT TEAM LEADER
B. Purevtseren (Ph.D)
Dept. of Telecommunication Engineering, SICT, MUST (Antenna Laboratory)
e-mail: Purevtseren_b@must.edu.mn
Professor B. Otgonbayar (Ph.D)
School of ICT (SICT) / Department of Telecommunication Engineering
Email: otgonbayar_b@must.edu.mn
RESEARCH TEAM MEMBER
Ass. Professor Kishikawa Hiroki (Ph.D)
Tokushima University / Faculty of Science and Technology
Email: kishikawa.Hiroki@tokushima-u.ac.jp
JAPANESE PROJECT TEAM LEADER
A STUDY ON THE DEVELOPMENT OF SMART SYSTEMS FOR INDUSTRIAL, SERVICE, AND DOMESTIC APPLICATIONS USING ADVANCED TECHNOLOGIES
Scan me