## Slide 1
1. PROBLEM & OBJECTIVES
• Problem : artificial with knees user walking load , energy power spending high .
• Inactive artificial knee under load accustomed incompatible ; active system weight , energy power expensive .
• Objective : MBD, fMBD /ANCF, flexible contact and real walking data together energy power economical mechanism indicator to establish .
2. METHODS & COLLABORATION
• Base : B.Dondogjamt’s closed link and flexible MBD with contact .
• Model : ANCF elastic body + contact power + artificial knee slider-link mechanism .
• Test : CFRP material ; IMU 100 Hz + treadmill GRF 1000 Hz.
• Processing : MATLAB, DAE, Runge- Kutta Gill, cross-correlation, Butterworth, gait-cycle normalization.
3. KEY RESULTS, TECHNOLOGY / PRODUCT
KEY RESULTS
• Flexible contact GRF​ 61.35% reduction in walking and 34.22% reduction in running ( B. Dondogjamts , 2021).
• 2 peaks for walking , 1 peak for running and damping​ caused period difference determined .
• CFRP testing compression The force reaches 1.4 N. even though it is stable , deformation continued .
• Knee angle –slider transition relationship linear not ; critical movement limits by MBD defined .
• Real gait : cycle 1.05 s; stance 62%; swing 0.40 s; foot Height 0.22 m.
• GRF: impact ~1000 N, push-off ~800 N (80%); hip 0–40°, knee 0–50°, ankle −10°...+20°.
TECHNOLOGY / PRODUCT
• Biological contact → flexible material → artificial knee → real walking data connected calculation design flow .
• 4 studies seed result combined mechanism parameters , load , energy evaluation .
4. APPLICATIONS & BUSINESS POTENTIAL
PRACTICAL APPLICATIONS
• Artificial knee , orthosis / exoskeleton , rehabilitation fix walking evaluation .
• Sports biomechanics , foot robots , users adjusted help device .
BUSINESS POTENTIAL
• Simulation-based mechanism design and verification service.
• Hospital , rehabilitation fix center , prosthesis pilot with manufacturer .
• 3D printing , technology transmission , license , joint product .
PARTNERSHIP, IMPACT & NEXT STEPS
6. CONTACT & BUSINESS MATCHING
Sub coordinator: E.Naranbaatar| Lead Researcher: B.Dondogjamts, Ch.Purevdorj,
Japan Counterpart: Hiroaki Wagatsuma, Kyutech
MONGOLIAN TEAM LEADER
E. Naranbaatar, Ph.D
Mongolian University of Science and Technology, SMET
JAPANESE COUNTERPART
Hiroaki Wagatsuma, Professor
Kyushu Institute of Technology, Life Science and Systems Engineering
SUB-COORDINATOR
JAPANESE SUB- COUNTERPART
Hiroki Kishikawa , Professor
University of Tokushima
B. Otgonbayar , Professor
Mongolian University of Science and Technology, SICT
RESEARCH FIELD
Automation, system engineering
J23A16-4
The development of industrial, service and intelligent systems based on advanced technologies
Intelligent robotics application for industry and service
Keyword : Robotics, Dynamics, MBD, Legged robotics
MUST – SMET • Kyushu Institute of Technology • MJEED–JICA J23A16